## Slide 1: Introduction to Electrical Engineering

## Slide 2: Overview
Physical Principles and Basic Concepts
Direct Current Circuits
Electric and Magnetic Fields
Alternating Current Technology
Wrap-Up and Outlook

## Slide 3: Physical Principles and Basic Concepts
Electric Charge
Band Structure
Current
Voltage
Ohm‘s Law
Resistors
Ideal Voltage & Current Sources
Electric Power

## Slide 4: The World Is Not What It Seems
All the “stuff“ around us consists of atoms.
And atoms are nearly empty.
hydrogen
helium
proton
electron
nucleus:
2 protons, 2 neutrons
electron cloud:
2 electrons
electric charge

## Slide 5: Periodic Table of Elements

## Slide 6: Coulomb Force
positive and negative charges attract each other
simple atomic model: balance with centrifugal force
 stable electron orbits

## Slide 7: Electric Charge
elemantary charge:
(coulomb)
: fundamental physical property
(odd number because some physical units were arbitrarily determined)
other fundamental forces: gravity (mass, only one not quantized?), strong (keeps atomic nuclei together) and weak (e.g., reason for radioactive beta decay) nuclear forces
not relevant for electrical engineering though: gravity very weak, nuclear forces very short-ranged

## Slide 8: International Systems of Units (SI)
just a convention
time
length
mass
electric current
thermodynamic temperature
amount of substance
luminous intensity
all other units derived
outer ring: SI base units
inner ring: constants

## Slide 9: Bohr Model
modern view: orbital model (location of electrons in atom determined by quantum-mechanical wave function  probability distribution)
models just try to approximate the world: more complex models capture more details
allowing only certain energies (orbits) of electrons  quantized!
higher potential energy

## Slide 10: Band Structure
Atomic nuclei have fixed positions in solids.
But the electron shells overlap.
 Higher-energetic electrons can move (drift) through solid matter.
carbon

## Slide 11: Electric Current
moving electrons  moving charges: electric current
(ampere)

## Slide 12: Drift Velocity

example:
copper wire of with

but starts everywhere in the conductor at the same time
is current density (measure of thermal stress on conductor)
typically, fuses in households
typically, copper cable used for lighting and for power circuits

## Slide 13: Conventional Current
arbitrarily defined as direction in which positive charges flow
battery

## Slide 14: Voltage
Voltage is the driving force of electric current.
relative quantity: potential difference between two points in space
electric potential : defined from potential energy of a charge
(volt)
symbol in German literature

## Slide 15: Types of Voltage Generation
generators (mechanical, often via turbines, e.g., from thermal energy)
batteries (chemical)
photovoltaic
piezoelectric
…

## Slide 16: Ohm‘s Law
(ohm)
electrical resistance
current-voltage characteristic
(I-V curve)

## Slide 17: Electrical Conductance
(siemens)
formerly: (mho)

## Slide 18: Specific Resistance
also called electrical resistivity
material | (Ωmm2/m)
silver | 0.016
copper (power cable) | 0.017 ... 0.018
gold | 0.022
aluminium | 0.027
constantan (Cu + Ni) | 0.5
quartz glass | 7.51023
material | 
silver | 0.016
copper (power cable) | 0.017 ... 0.018
gold | 0.022
aluminium | 0.027
constantan (Cu + Ni) | 0.5
quartz glass | 
at
example:
copper cable with and has
 wiring usually negligible

## Slide 19: Specific Conductance
also called electrical conductivity

## Slide 20: Conductor, Semiconductor, Insulator
examples: copper, silver, aluminium
examples: ceramic, rubber, oil, glass
examples: silicon, germanium, selenium

## Slide 21: Temperature Dependence of Resistivity
metallic conductors: resistivity increases with higher temperature (stronger vibrations of atoms, impeding the flow of electrons)
semiconductors: resistivity decreases with higher temperature (more electrons can jump to the conduction band, increasing the number of free charge carriers, i.e., electrons and holes)
insulators: decreases slightly with higher temperature

## Slide 22: Temperature Coefficient
NB: linear approximation only valid in limited temperature range
material | in K-1
iron | 
aluminium | 
gold | 
copper | 
silver | 
constantan | 
germanium | 
silicon | 
material | 
iron | 
aluminium | 
gold | 
copper | 
silver | 
constantan | 
germanium | 
silicon | 
metals: positive temperature coefficient (PTC)
semiconductors: negative temperature coefficient (NTC)
for

## Slide 23: Example: Tungsten Filament
A light bulb contains a tungsten filament with a diameter of and a length of , which is operated at a constant voltage of .
Current through the tungsten wire when the bulb is switched on in cold state ():
at operating temperature ():
quadratic term: more accurate approximation for large temperature differences

## Slide 24: Electrical Loads
any component/device consuming electrical power
resistive load:
electrical energy is converted into heat or light (e.g., incandescent bulbs)
resistor (also a resistive load itself):
specific component to limit/control the current in electrical circuits (precise, known amount of resistance)
capacitive & inductive loads: energy temporarily stored in electric or magnetic fields

## Slide 25: Resistors
E6 (±20%) | E12 (±10%) | E24 (±5%)
1,0 | 1,0 | 1,0
 |  | 1,1
 | 1,2 | 1,2
 |  | 1,3
1,5 | 1,5 | 1,5
 |  | 1,6
 | 1,8 | 1,8
 |  | 2,0
2,2 | 2,2 | 2,2
 |  | 2,4
 | 2,7 | 2,7
 |  | 3,0
E6 (±20%) | E12 (±10%) | E24 (±5%)
3,3 | 3,3 | 3,3
 |  | 3,6
 | 3,9 | 3,9
 |  | 4,3
4,7 | 4,7 | 4,7
 |  | 5,1
 | 5,6 | 5,6
 |  | 6,2
6,8 | 6,8 | 6,8
 |  | 7,5
 | 8,2 | 8,2
 |  | 9,1

## Slide 26: Ideal Voltage Source
battery
maintains a fixed voltage across its two terminals (independent of the output current or load resistance)
model!
also:

## Slide 27: Ideal Current Source
generates a fixed current (independent of the voltage changes across it)
Usually, there are only voltage supplies.
However, the behavior of the current source model can be constructed using circuitry.
also:

## Slide 28: Work
electrical energy dissipated in a resistor:
if current or voltage varies over time:

## Slide 29: Electric Power
(watt)
example:
A cooler bag for connection to the electrical system of a car draws a constant current of , resulting in . So, in 8 hours .

## Slide 30: Summary
A basic electrical circuit consists of
a voltage source (providing the electrical potential difference that drives the current, like a battery or generator),
conductive pathways (wires or traces allowing the current to flow from the source to the load and back),
and a load (device using the electrical energy, such as a light bulb, motor, or computer).
Ohm‘s law: